## Slide 1
Hybrid Cord Patents — Wear / Mileage Analysis
Zero-degree belt cords in PCR tires · General hybrid vs. Nylon-Aramid · PatSeer landscape, 1,172 PCR patents

## Slide 2
Scope & Method
• Source: PatSeer zero-degree belt landscape — 1,816 families, screened to 1,172 passenger-car-radial (PCR) zero-degree (cap-ply / overlay / jointless-band) patents.
• Two hybrid-cord cohorts defined from patent text:
– General hybrid cords — explicit hybrid wording or any two-material cord co-occurrence: 507 patents
– Nylon-Aramid cords (focus) — aramid + nylon hybrid: 318 patents
• Wear/mileage detection: lexicon over title, abstract, claims, description and PatSeer AI summaries.
• Theme tagging: BENEFIT (wear resistance / mileage / tread life) vs. DEFENSIVE (fixing uneven / irregular wear).
• Caveat: keyword + co-occurrence based — high recall; verify borderline cases against claims.

## Slide 3
Headline Finding
• General hybrid: 199 of 507 (39%) make a wear/mileage claim.
• Nylon-Aramid: 115 of 318 (36%) make a wear/mileage claim.
• The zero-degree cord is NOT primarily a mileage technology — its wear effect is indirect (crown stiffness & footprint uniformity).
• Key difference: Nylon-Aramid skews more DEFENSIVE — a larger share fixes uneven wear the stiff aramid cap ply introduces, rather than claiming a clean mileage win.

## Slide 4
Wear Posture — Claiming a Benefit vs. Fixing Uneven Wear
• Each bar = 100% of that cohort's wear patents, split by what they claim.
– Benefit only = a wear/mileage win, no problem mentioned.
– Defensive = fixes uneven / irregular wear.
• Nylon-Aramid is more defensive: 22 defensive-only vs only 10 'both'.
• General hybrid is the reverse: 44 'both' vs 24 defensive-only.
• Why: stiff aramid helps footprint uniformity, but its stiffness step can trigger uneven wear that must be engineered out.

## Slide 5
Claimed Wear Mechanisms
• Wear effects attributed mainly to cord modulus / material and circumferential rigidity / in-plane shear.
• Then growth & tread-profile control and footprint / contact-pressure uniformity.
• Confirms mechanism is structural (stiffness, footprint) — not tread-compound abrasion chemistry.
• Patents may count under several mechanisms.

## Slide 6
Who Owns the Nylon-Aramid Wear IP
• Sumitomo, Bridgestone, Goodyear lead; Continental, AlliedSignal (Honeywell) and Kumho also active.
• Several Continental and Kumho entries are legally ALIVE — current freedom-to-operate relevance.
• AlliedSignal patents frame treadwear via in-plane shear modulus of the fiber belt.

## Slide 7
Representative Nylon-Aramid Wear Patents
• EP4335661A1 — SUMITOMO RUBBER IND LTD (2022, ALIVE)
– The reinforced belt layer ensures structural integrity and reduces the likelihood of breakage, extending tire life.
• DE102016223304B4 — CONTINENTAL REIFEN DEUTSCH (2016, ALIVE)
– The belt bandage is applied in a single layer, with the side sections arranged to provide a more uniform abrasion and improved rolling resistance compared to the center section.
• CN106457914A — CONTINENTAL REIFEN DEUTSCH (2014, ALIVE)
– Additionally, conventional belts have limited circumferential stiffness, which can cause uneven wear and reduce tire performance.
• KR20130067396A — KUMHO TIRE CO INC (2011, ALIVE)
– The cap ply design allows for even distribution of adhesion forces, preventing uneven wear and maintaining tire integrity.
• WO2018230265A1 — BRIDGESTONE CORP (2017, DEAD)
– The present invention addresses the problem of suppressing the occurrence, in a tire having a spiral cord layer formed by winding a reinforcement cord in a spiral shape, of uneven wear due to the spiral cord layer.
• US20040108037A1 — BOOZER MATTHEW (2002, DEAD)
– The use of high modulus at high stress cords in the second reinforcement plies allows the tire to flatten the transverse curvature at low and moderate speeds, improving wear performance.

## Slide 8
Deep Dive — How Nylon-Aramid Patents Solve Wear
• Researchers rarely chase abrasion resistance directly.
• The strategy: make the contact patch uniform & dimensionally stable.
• Aramid gives hoop stiffness → restrains crown growth → stable tread geometry → less slip/squirm wear.
• But aramid's stiffness step itself causes uneven wear — so most IP is about placing & grading that stiffness.

## Slide 9
Five Recurring Engineering Solutions
• 1. Dual-modulus / core-sheath cord (51%) — low-mod core (nylon/rayon/PET) + high-mod aramid sheath; soft to build, stiff in service.
– Goodyear EP2380755A2 (ALIVE): low-modulus core, 5–15 TPI, high-modulus outer filament.
• 2. Twist / cord-geometry tuning (64%) — twist, denier, filament count set where the modulus transition occurs.
• 3. Adhesion / dip engineering (61%) — epoxy pre-dip + RFL; less cord-rubber slip → less wear & edge separation.
– Goodyear US20160288575A1: single-end-dipped (SED) cords, no calendering.
• 4. Zoned / two-layer overlay (46%) — different cord/density across tread width to equalise contact pressure (the uneven-wear fix).
• 5. Positioning vs. grooves & geometry ratios (20%) — keep the stiffness step away from where wear initiates.

## Slide 10
The Uneven-Wear Fix: Zoned Density (live art)
• Continental EP3912833A1 (ALIVE): centre PET at 120 EPDM + PA4.6 side sections at 130 EPDM.
• Continental DE102016223304B4 (ALIVE): 3-section bandage, centre PA6.6 (470x2) + side sections for 'more uniform abrasion'.
• Sumitomo JP2018184071A (ALIVE): centre low density (Ec) + shoulder high density (Em) → even stiffness across the tread.
• Continental EP2048005B1 (ALIVE): tuned radius-to-width ratios so the stiffness discontinuity doesn't land at wear-initiation sites.
• Implication: the defensible path is stiffness PLACEMENT (zoning / grading), not a harder cord — and Continental & Sumitomo already hold live art here.

## Slide 11
Takeaways & Recommendations
• Wear/mileage is a SECONDARY, indirect benefit of hybrid zero-degree cords — led by stiffness and footprint control.
• For Nylon-Aramid specifically, manage the uneven-wear risk: the stiffness step at the cap-ply edge / over the reinforcing layer drives irregular wear.
• Design levers in the IP: dual-modulus cord, twist tuning, adhesion/dip, zoned/two-layer bandage, positioning vs. grooves.
• White space is narrow: zoned-density / modulus-grading is the proven path but Continental & Sumitomo hold live art — check freedom-to-operate.
• Next: tighten the Nylon-Aramid set to explicit co-twisted constructions; add rolling-resistance and high-speed-durability axes.